## Slide 1
KX-NTV150/160 Basic Specification
October 26, 2015
Specifications are subject to change without notice.
Panasonic System Networks PBX SE team

## Slide 2
1. Table of Contents
Chapter | Contents
1 | Overview
2 | Basic configuration
3 | AK and Conditions
Notes: 2

## Slide 3
Chapter 1 Overview

## Slide 4
11. System Overview
System Overview
Video Terminals(SIP)
PBX
NTV160
Door Opener
NTV150
SIP
ONVIF
Audio Terminals
Web Viewer
Viewer Application
NTV150/160 are IP Voice terminals with camera.
They are one of the PBX terminals that are handled as SIP extension.
Notes: 4
<Policy>
- Easy installation and maintenance are basic policy.
- Voice Quality and PBX related feature are differentiating from network camera.
- NTV Series can be used as SIP video terminals and also monitoring camera.
- NTV Series connect to only Panasonic PBX.

## Slide 5
12. System Description
Item | Description
NTV150 | Communication IP Camera
NTV160 | Video door phone
Video teminal | HDV430, SIP Softphone application
Audio teminal | PBX Audio phone (NTseries, DPT, APT etc.)
Viewer | Embedded Web Viewer by NTV150,NTV160
 | Viewer Application
KX-NTV150 and KX-NTV160 can be connected to only NS/NSX series as SIP extension.
Notes: 5

## Slide 6
13. Compatible PBX
Model | Required Activation Key
NS Seriese (300/500/700/1000) v4.3 or later | IP Extension Activation Key for NT series
NSX Seriese (1000/2000) | Panasonic Peripheral Device Activation key
  Compatible PBX
  NTV150/160 can ONLY work with following Panasonic PBX.
  These terminals can NOT work with 3rd party PBX, SIP server and other Panasonic
  PBX such as NCP
Notes: 6

## Slide 7
The voice terminal with camera will offer a variety usage !
14. Main features
Camera control !
Video and Audio communication !
email
Event action !
Multiple
connection !
Audio
Video
2
4 6
8
Control by DTMF
7 9
5: Open the door
outgoing
- Voice
- Video motion
Audio
Video
Video
Max.10
Video connection
Monitoring
- Pan
- Tilt
- Zoom
Notes: 7

## Slide 8
Chapter 2 Basic Configuration

## Slide 9
21. KX-NTV150 / 160
KX-NTV150 : Communication SIP Camera - PoE / AC adapter
- LAN / Wi-Fi - Built-in Speaker and Microphone - Call button
- Indoor use only KX-NTV160 : SIP based Video Doorphone - PoE only
- LAN only - Built-in Speaker and Microphone - Call button - IP-Grade : IP43
IP43：Ingress Protection dust-proof grade 4, waterproof grade 3
Notes: 9

## Slide 10
KX-NTV150 : Communication SIP Camera
Rear Side
・AC Adapter Power Jack
・Ethernet Port (RJ-45)
・External I/O Port
・WPS/Reset Button
Call Button
Status LED
Speaker
Camera Lens
Microphone
22. KX-NTV150
Notes: 10

## Slide 11
KX-NTV150 : Communication SIP Camera
Status LED | Indicate communication camera status
Hardware Key | Call button : Make a call, Cancel a call WPS/Reset Button - WPS : Push button more than 2 seconds and less than 10 seconds - System Reset : Push button more than 30 seconds.
Speaker / Microphone | Built-in Speaker / Built-in Microphone
Installation Method | Put on the desk, fixed by stand,
Ethernet Port | 10Base-T/100BaseTx, RJ-45 connector, PoE (IEEE802.3af) supported
Wireless | Wi-Fi (802.11b/g/n, 2.4GHz) Supported, internal Wi-Fi antenna (2x2)
Power Supply | 1.use AC adapter option KX-A239 2.use PoE
External I/O | Input: 1ch -> digital input: for example, detect that buzzer button was pushed Output: 1ch -> Main usage: drive relay parts for door openner
IP Protection | No (Indoor use only)
23. KX-NTV150 Specification
Notes: 11

## Slide 12
KX-NTV160 : Video door phone
Rear Side
・Ethernet Port (RJ-45)
・External I/O Port
Camera Lens
Light Source LED
Speaker
Call Button
Status LED
Reset Button
Microphone
24. KX-NTV160
Notes: 12

## Slide 13
KX-NTV160 : Video door phone
Status LED | Indicate video door phone status
Light Source LED | Emitting for visible in night, emitting color: ”Warm-white”
Hardware Key | ･Call button: Make a call ･Reset button: System reset Push button more than 30 seconds.
Speaker / Microphone | Built-in Speaker / Built-in Microphone
Installation Method | Wall mounted
Ethernet Port | 10Base-T/100BaseTx, RJ-45 connector, PoE (IEEE802.3af) supported
Power Supply | use PoE only
External I/O | Input: 1ch -> digital input: for example, detect that switch was pushed Output: 1ch -> Main usage: drive relay parts for door openner
IP Protection | Equivalent of IP43 at installed condition
25. KX-NTV160 Specification
Notes: 13

## Slide 14
26. Main features
1. Video and Audio communication
NTV150/160 can make a video and audio call communication.
2. Camera Control
NTV150/160 have ePTZ and door opener which are controlled by DTMF from PBX terminals.
ePTZ : electronic pan-tilt-zoom
Notes: 14

## Slide 15
Model | Remarks
KX-HDV430 | Panasonic SIP Phone
SIP Softphone application | Bria SIP softphone (COUNTERPATH)
KX-NTV supports following Panasonic PT and IP phones.
26. Main features
Video Terminals
Audio Terminals
Model | Remarks
PBX Audio phone | NTseries, DPT, APT, SLT, SIP, etc.
Compatible Terminals
Notes: 15

## Slide 16
26. Main features
3. Event Action
Notification is available by event setting of NTV150/160.
SIP outgoing
e-mail
e-mail
snapshot
Motion detection
Voice detection
Digital Input etc.
Notes: 16

## Slide 17
26. Main features
Schedule | Trigger | Action
- Sun, Mon, Tue, Wed, Thu, Fri, Sat - Time “Always” “From to [hh:mm]” | - Video motion detection - Voice detection - Periodically - Digital input - System boot - Recording notify - Camera tampering detection - Manual triggers | - SIP Outgoing - Server (Email or FTP or HTTP or Network storage )
Event Setting
Notes: 17
-Server Name-
default : blank
- Server Type-
Email or FTP or HTTP or Network storage selected by radio button
When Event is set on Motion detection
-Media Type-
Snapshot or Video clip or System log selected by radio button
default : no check

## Slide 18
26. Main features
4. Multiple Connection
NTV150/160 can support Maximum 10 multiple video connection.
SIP Call
Web access or
Viewer APP
by RTSP Protocol
Audio
Video
:
:
Total MAX
10 Connections
9 Connections
(Max 10)
1 Connection
Video
Video
Video
NTV150/160
Video
Video
:
:
Notes: 18

## Slide 19
Chapter 3 AK and Conditions

## Slide 20
AK for KX-NTV is required for KX-NTV instead of User AK in NSX series. AK for IP extension is required for KX-NTV like a NT phone in NS series.
31. Activation Key
To connect | AK for IP-PT (KX-NSM) | AK for Peripheral Device (KX-NSXN )
KX-NS series | Required | 
KX-NSX series |  | Required
KX-NTV150
KX-NTV160

## Slide 21
32. Conditions
Output port control
It will be controlled during the talking.
Only NT55x,NT54x and SIP terminals can send DTMF control signal.
NTV150/160
Embedded WEB Server | OS: Windows 7 / 8 / 10 Browser: IE7 / IE8 / IE9 / IE10 / IE11 / Firefox
Embedded WEB Accounts | 20 accounts admin / operator / Viewer
Embedded WEB Access Restriction | Up to 10 users
Viewer
SIP Outgoing
When push the call button, it will start to make a call.
One telephone number can be assigned for destination. (up to 32 digits)
Notes: 21

## Slide 22
32. Conditions
NTV150 only
Wi-Fi
TYPE | IEEE802.11 b/g/n 2.4GHz
Antenna | 2x2
Channel | 1-13ch(for NE etc. except US) / 1-11ch(for US)
Security (Encryption) | WEP(64bit/128bit), WPA(TKIP/AES), WPA2(TKIP/AES)
WPS (Wi-Fi Protected Setup) | supported
NTV150 | 0 ~ 40 degrees Celsius (Operating range)
NTV160 | -10 ~ 50 degrees Celsius (Operating range)
Ambient Temperature
NTV150/160
Notes: 22
NTV160は積極的に屋外使用とは言わない。 社内の屋外製品規定に適合していないため。

## Slide 23
Thank you !

## Slide 24
Appendix

## Slide 25
Appendix
  Vivotek ST7501 and iViewer
  Vivotek ST7501(CMS) and iViewer(Viewer APP for Mobile) can connect to NTV150/160 and User can operate all function of them .
  CMS(Central Management Software)
Features
- 32-channel Live Video Monitoring
- PTZ/ePTZ Function Control
- Event Alarm Management
- Overall Device Management through Intuitive E-map Feature
- Two-way Audio, Multi-channel Audio Broadcast
- Instant Replay & Playback on Live Client
- Auto Stream Size for Reducing Display Loading
- Directly Set up Basic Parameters for Cameras
Viewer Application
Vivotek ST7501(CMS)

## Slide 26
Viewer Application
Features
- Multi-channel Live View & Single Channel Playback
- Variable-Speed Fast-Forward and Reverse for Playback
- Multi-Stream Selection
- Vertical (Portrait) or Horizontal (Landscape) Mode Rotation
- Snapshot Option
- PTZ Control
- PiP (Picture in Picture) Control
- One Way Audio
Supported OS: iOS 6.0 or late, Android 2.3.3 or above
  iViewer
Appendix

## Slide 27
Feature |  | KX-NTV150 / KX-NTV160
Image Sensor | Type | 1/3.2" Progressive CMOS
Lens | Type | Fixed-focal
 | Focus Range | ∞ ~ 0.4 (TBD) m
Field of View (Image aspect=4:3) | Horizontal | 92°
 | Vertical | 70°
 | Diagonal | 115°
Field of View (Image aspect=16:9) | Horizontal | 92°
 | Vertical | 52°
 | Diagonal | 106°
    Camera Block
Appendix

## Slide 28
Feature |  | KX-NTV150,KX-NTV160 | 
Number of Stream |  | 3 (Stream1, Stream2,Stream3) Stream1:for RTSP, Stream2:for SIP Stream3:for RTSP of mobile phone (Resolution is fixed QVGA(320x240)) | 
Codec |  | Support H.264 and JPEG (only for RTSP) | 
Resolution |  | (Stream1 and 2) 1600x1200, 1280x960, 1280x720, 1024x768, 640x480, 640x360, 386x216, 352x288, 320x240,176x144 | 
Frame rate | Maximum frame rate setting | (Stream1 and 2) 1,2,3,5,8,10,12,15,20,25,30fps, customized(1 - 30fps) | 
 | Maximum performance | (Stream1 and 2) H.264: 30fps@1600x1200 30fps@1280x720 | (Stream1 and 2) MJPEG: 30fps@1600x1200 30fps@1280x720
    Video (Live View Settings)
Appendix

## Slide 29
Feature |  | KX-NTV150,KX-NTV160
Echo Canceller |  | Include function of echo canceller Half Duplex
Mute for Microphone | Activate | ON/OFF
Volume control for Speaker | Microphone input gain | Level tuning (1~100%)
Mute for Speaker | Activate | ON/OFF
Volume control for Speaker | Speaker output gain | Level tuning (1~100%)
Codec |  | Support G.711, G.722(Only for SIP), G.729a(Only for SIP) select u-law or a-law
    Audio
Appendix

## Slide 30
Feature | KX-NTV150,KX-NTV160
Network Interface | 1 x RJ45, 10Base-T/100BaseTx
DTMF | Out band (RFC2833) / SIP INFO
TONE | Busy Tone / Ring Back Tone / Reorder Tone / Key Tone / Confirmation Tone
Embedded WEB GUI Language | English, Spanish, French, Italian, German, Portuguese, Russian
RTP / RTCP | Yes
RTCP-XR (RFC3611) & SIP PUBLISH | No
DNS-SRV (RFC3263) | No
LLDP / LLDP-MED | No
LDAPv3 | No
SNTP | Yes
NAT traversal | No
  SIP Terminal Features
Appendix

## Slide 31
Feature (Security) | KX-NTV150,KX-NTV160
Attack IP Packet Protection | Yes
SIP INVITE Attack Protection | No
IEEE802.1x | Yes
QoS | Yes
Digest Authentication using MD5 | Yes
AES Key Sizes | 128 / 192 / 256 bits
RSA Key Sizes | 2048 / 4096 bits
Admin/User Configuration Mode | No
WIFI WEP | 64bit/128bit(*onlyNTV150)
WIFI WPA(TKIP/AES) | Yes(*onlyNTV150)
WIFI WPA2(TKIP/AES) | Yes(*onlyNTV150)
  SIP Terminal Features
Appendix

## Slide 32
Revision
Date | No. | Change
October 26, 2015 | All | First draft
Notes: 32